## Slide 1: Solid-Based Rapid Prototyping Systems
Starting material is a solid
Solid-based RP systems include the following processes:
  Laminated object manufacturing
  Fused deposition modeling

## Slide 2: Fused Deposition Modeling- FDM
Developed by S. Scott Crump in the late 1980s
Commercialized in early 1990s
Principle of laying down molten material in layers
Nozzle is heated to melt the thermoplastics material
The print head moves on X-Y Axis to draw the layer
The platform drops down on Z for each layer
Separate dissolvable support material
Several material and color options
Fused Deposition Modeling (FDM) is an additive manufacturing technology.
Used for modeling, prototyping and production applications.

## Slide 3: Fused Deposition Modeling (FDM)
The fused deposition modeling (FDM) technology was developed by S. Scott Crump in the late 1980s and was commercialized in 1990. The double material approach was developed by Stratasys in 1999.
Current market leaders
Stratasys, Inc.
Stratasys Dimension SST 1200
"Ribbon Tetrus" (Carlo Séquin)
Courtesy, Dr. Robin Richards, University College London, UK
www.nybro.com.au

## Slide 4
Step 1: Pre-processing
A CAD model is constructed, then converted into the STL format ready for the FDM process.
Step 2:Production
FDM machine processes .STL file by creating sliced layers of the model.
The first layer of the physical model is created
The model is then lowered by the thickness of the next layer.
The process is repeated until completion of the model.
FDM process steps

## Slide 5
Step 3: Post processing
The model and any supports are removed by washing or stripping it away.
The surface of the model is then finished and cleaned

## Slide 7: Fused Deposition Modeling (FDM) Process
A spool of thermoplastic wire (typically acrylonitrile butadiene styrene (ABS)) with a 0.012 in (300 μm) diameter is continuously supplied to a nozzle
The nozzle heats up the wire and extrudes a hot, viscos strand (like squeezing toothpaste of of a tube).
A computer controls the nozzle movement along the x- and y-axes, and each cross-section of the prototype is produced by melting the plastic wire that solidifies on cooling.
In the newest models, a second nozzle carries a support wax that can easily be removed afterward, allowing construction of more complex parts. The most common support material is marketed by Stratasys under the name WaterWorks

## Slide 8
ADVANTAGES
FDM is clean, simple to use.
Thermoplastic parts can endure exposure to heat, chemical, humid or dry environments, mechanical stress.
Soluble support materials make it possible to produce complex geometric and cavities that would be difficult to build with traditional manufacturing methods.
Economical (inexpensive materials)
Enables multiple colors
Easy to build DIY kits (one of the most common technologies for home 3D printing)
A wide range of materials possible by loading the polymer

## Slide 9
DISADVANTAGES
Materials suite currently limited to thermoplastics.
The extrusion head must continue moving or else material bumps up.
Supports are required.
Part strength is weak perpendicular to the build axis.
As layer increases, the build up increases.
Temperature fluctuation during production could lead to delamination.

## Slide 10
KEY APPLICATION AREAS
  Conceptual Models
  Engineering Models
  Functional Testing Prototypes
  Aerospace-human supporting rovers
  Automotive – automobile parts
  Commercial – mobile covers
  Medical – drug injection system

## Slide 11: Fused Deposition Modeling (FDM)
KEY APPLICATION AREAS
Maximum build size | 20” x 20” x 20”
Resolution in (x,y) | +/- (0.002” - 0.005”)
Resolution in z | +/- (0.002” - 0.01”)
Speed | Slow
Cost | Medium
Available materials | Thermoplastics (ABS, PC, ULTEM…)
KEY METRICS
ADVANTAGES
DISADVANTAGES
Economical (inexpensive materials)
Enables multiple colors
Easy to build DIY kits (one of the most common technologies for home 3D printing)
A wide range of materials possible by loading the polymer
Materials suite currently limited to thermoplastics (may be resolved by loading)
  Conceptual Models
  Engineering Models
  Functional Testing Prototypes
www.redeyeondemand.com

## Slide 12
FDM: companies and applications
FDM™ is a patented technology of Stratasys™ Inc.
Monkey Cinquefoil Designed by Prof Carlo Sequin, UC Berkeley
5 monkey-saddles closed into a single edged toroidal ring
Gear assembly Toy design using FDM models of different colors