## Slide 1
Metal removal by electrochemical process.
Non-traditional machining process
Energy Domain – Electro-chemical category.
For machining extremely hard materials or materials that are difficult to machine using conventional methods.
ELECTRO CHEMICAL MACHINING

## Slide 2
External as well as internal geometries can be machined.
For machining or cutting the intricate contours or cavities in hard materials such as titanium, Hastelloy, Kovar, Inconel, Carbide etc.
ELECTRO CHEMICAL MACHINING
Limited to electrically conductive materials.

## Slide 3
It is based on Faraday’s laws of electrolysis (electroplating).
ECM is characterized as the opposite of electrochemical or galvanic coating or deposition process.
Similar to EDM. However, in ECM there is no tool wear.

## Slide 4
ECM Fundamentals

## Slide 5
Electrolysis of a copper sulphate solution

## Slide 6
As per polarity, the chemical reactions occurring at the anode and cathode are called anodic and cathodic reactions respectively.

## Slide 8
Due
The rate of dissolution depends upon:
The ionic charge
Atomic weight
The current and
The time of current passage.
At the anode, the metal dissolves electrochemically.

## Slide 9
The electrode shape remains unaltered during the electrolysis process. This is the most relevant feature of ECM being used as a metal shaping process.
At the cathode, only the hydrogen gas is evolved.
The rate of dissolution is not influenced by the hardness of the work piece material or any other metal characteristics.

## Slide 12
Mechanism of Material Removal in ECM
The work piece and tool are the anode and cathode respectively.
In the electrolytic cell a constant potential difference, usually of about 10 V is applied across them.
A suitable electrolyte, for example an aqueous sodium chloride (table salt) solution is commonly chosen.
The rate at which metal is then removed from the anode is approximately in inverse proportion to the distance between the electrodes.

## Slide 13
In-order to remove the products of machining, the electrolyte is pumped through the gap between the two electrodes.
As the machining proceeds there is a simultaneous movement of the cathode towards the anode.
The width of the gap along the electrode length will gradually tend towards a steady-state value.
Under such conditions, a shape which is roughly complementary to that of the cathode will be reproduced on the anode.

## Slide 15
In the ECM setup, as the gap between tool and work piece is small, a low and constant voltage of around 10 V is applied across the electric circuit. The current density is however high.
Power System
Electrolyte Filtration and Delivery System
The electrolyte system consists of the electrolyte storage tank, fairly strong pump, filter, sludge removal system and treatment units.

## Slide 16
The electrolyte chosen is such that the shape of cathode is not changed during electrolysis.
To remove the products of machining and to reduce the undesirable effects which may arise with the gases generated at the cathode and electrical heating, the electrolyte is pumped at a rate of 2 to 30 m/s, through the gap between the electrodes.

## Slide 17
Tool Feed system
In the ECM setup, a constant gap between tool and work piece is to be maintained.
Tool Material Properties
Should be a good conductor of electricity.
Should be rigid enough to take up load and the fluid pressure.
Easily formable and machinable to the desired shape.

## Slide 18
Other materials:
Aluminium, graphite, bronze, platinum, and tungsten carbide.
Tool Material
Common materials:
Copper, Brass, Titanium, Copper-Tungsten and Stainless steels.

## Slide 19
Power Supply: It’s Type, Voltage, Current and Current density.
Electrolyte: Type, Temperature, Flow rate, Pressure and Dilution.
Machine setting parameters: Working gap, Overcut and Feed rate.
Electrode material: Type of the material used.
ECM Process Parameters