## Slide 1: MODULE 4
SPUR GEARS AND GEAR TRAINS

## Slide 2: Syllabus:
Module – 4
Spur Gears: Gear terminology, law of gearing, path of contact, arc of contact, contact ratio of spur gear. Interference in involute gears, methods of avoiding interference, back lash, condition for minimum number of teeth to avoid interference, expressions for arc of contact and path of contact
Gear Trains: Simple gear trains, compound gear trains. Epicyclic gear trains: a Algebraic and tabular methods of finding velocity ratio of epicyclic gear trains, torque calculation in epicyclic gear trains.
Duration: 10 Hours

## Slide 3
GEARS
Gears are toothed wheels used to transmit motion or power (mechanical energy) accurately, in the form of rotational movement from one shaft to another preferably, if centre distance between the two shafts is small.

## Slide 4
Power transmission systems
Belt/Rope Drives - Large center distance of the shafts
Chain Drives - Medium center distance of the shafts
Gear Drives - Small center distance of the shafts

## Slide 5
Friction Discs

## Slide 6
Gears may be classified according to the relative position of the axes of revolution. The axes may be parallel, intersecting and neither parallel nor intersecting.
1. Gears for connecting parallel shafts
Spur Gears: External contact Internal contact
Classification

## Slide 7
2. Gears for connecting intersecting shafts – Bevel Gears

## Slide 8
Crossed-helical gears
Worm & Worm Wheel
3. Gears for neither parallel nor intersecting shafts.

## Slide 9
Spur Gear

## Slide 10
Spiral bevel gears
Straight bevel gears
Bevel gears

## Slide 11
Parallel Helical gears Heringbone gears
(Double Helical gears)
Helical gears

## Slide 12
Worm and Worm Wheel

## Slide 13
Rack and Pinion

## Slide 14
Gear Box

## Slide 15: Classification:
According to the relative position of the axes of shafts on which the gears are mounted:

## Slide 16
      2. According to the peripheral velocity of gears:
        Low velocity gears (<3 m/s)
        Medium velocity gears (3<15 >m/s)
        High velocity gears(>15 m/s)
      3. According to the position of teeth on gear surface:
Straight teeth – Ex: spur gear
Inclined teeth – Ex: helical gear
Curved teeth – Ex: spiral gear
4. According to the type of gearing:
Internal gearing: gears mesh internally and they rotate in same direction.
External gearing: gears mesh externally and they rotate in opposite direction.

## Slide 17: Spur gears:
Gears whose axes are parallel and whose teeth are parallel to center line of the gears are called spur gears.
Terminology:

## Slide 18
Pitch Circle:
An imaginary circle which passes through the pitch point having its centre
at the axis of the gear, upon which all calculations are made.
Pitch Diameter:
it is the diameter of the pitch circle.
Pitch Surface:
it is the surface of the pitch cylinder.
Pitch Point :
The point of contact of two pitch circles is known as the Pitch point.
Line of Centers:
A line through the centers of rotation of a pair of mating gears is the line of centers.
Pitch Cylinders:
Pitch cylinders of a pair of gears in mesh are the imaginary friction cylinders, which by pure rolling together, transmit the same motion as the pair of gears.

## Slide 19
Pinion:
It is the smaller and usually the driving gear of a pair of mated
Rack:
It is a part of a gear while of infinite diameter
Pitch Line:
It is a part of the pitch circle of a rack and is a Straight line
Circular Pitch:
it is the distance measured along the circumference of the pitch circle from a point on one tooth to the correspond­ing point on the adjacent tooth

## Slide 20
Diametric Pitch
It is the number of teeth per unit length for Pitch circle diameter in inches
Module (m):
it is the ratio of the pitch diameter to the number Of teeth. The term is used in S.I. units in place of diametric pitch.

## Slide 21
Gear Ratio (G):
It is the ratio of the number of teeth on the gear to that on the pinion.
Also,
T = number of teeth on the gear,
t = number of teeth on the pinion.
Velocity Ratio (VR):
The velocity ratio is defined as the ratio of Angular velocity of the follower to the angular velocity of the driving Gear.
Let
Where
d = pitch diameter
T = number of teeth
W = angular velocity (rad/s)
N = angular velocity (rpm)
Subscript 1 = driver, 2 = follower
VR = angular velocity of follower
Angular velocity of driver

## Slide 22
Addendum Circle
It is a circle passing through the tips of the teeth
Addendum
It is the radial height of a tooth above the pitch circle.
Its standard value is one module.
Dedendum or Root Circle
It is a circle passing through the roots of the teeth
Dedendum
It is the radial depth of a tooth below the pitch circle.
Its standard value is 1.157 m.
Clearance
Radial difference between the addendum and the Dedendum of a tooth. Thus, Addendum circle diameter = d + 2m
Dedendum circle diameter = d - 2 x 1.157 m
Clearance = 1.157 m - m = 0.157m

## Slide 23
Full Depth of Teeth
It is the total radial depth of the tooth space.
Full depth = Addendum + Dedendum
Working Depth of Teeth
The maximum depth to which a tooth Penetrates into the tooth space of the mating gear is the working Depth of teeth.
Working depth = Sum of addendums of the two gears.
Space Width
It is the width of the tooth space along the pitch circle.
Tooth Thickness
It is the thickness of the tooth measured along The pitch circle.
Backlash
It is the difference between the space width and the Tooth thickness along the pitch circle.
Backlash = Space width - Tooth thickness

## Slide 24
Face Width
The length of the tooth parallel to the gear axis is the Face width.
Top Land
It is the surface of the top of the tooth.
Bottom Land
The surface of the bottom of the tooth between the adjacent fillets.
Face Tooth
surface between the pitch circle and the top land.
Flank
Tooth surface between the pitch circle and the bottom land Including fillet.
Fillet
It is the curved portion of the tooth flank at the root circle.

## Slide 25
Line of Action or Pressure Line
The force, which the driving tooth exerts on the driven tooth, is along a line from the pitch point to the point of contact of the two teeth. This line is also the common normal at the point of contact of the mating gears and is known as the line of action or the pressure line.
Pressure Angle or Angle of Obliquity (cp)
The angle between the pressure line and the common tangent to the pitch circles is known as the pressure angle or the angle of obliquity
For more power transmission and lesser pressure on the beams, pressure angle must be kept small. Standard pressure angles are 20° and 25°. Gears with 14.5° pressure angles have become almost obsolete

## Slide 26
Force perpendicular at f
Φ = 14.5˚
Φ = 20˚
Φ = 25˚
Pressure Angle

## Slide 27
Angle of Action
It is the angle turned by a gear from e beginning of engagement to the end of engagement of a pair of teeth, i.e. the angle turned by arcs of contact of respective gear wheels
Similarly, angle of approach and angle of recess can be defined.
The angle will have different values for the driving and the driven gears.
Contact Ratio
It is the angle of action divided by the pitch angle.

## Slide 29
Involute teeth

## Slide 30
Cycloidal teeth

## Slide 31
Features | Involute Profile | Cycloidal Profile
Definition | Locus of a point on a straight line which rolls without slipping on the circumference of circle (or if the curve is involute in nature then teeth is called involute teeth) | Locus of a point on a circle which rolls without slipping on the circumference of circle (or if the curve is involute in nature then teeth is called involute teeth)
Figure |  | 
Pressure angle | Constant thought the engagement. | Varies from commencement to end
Profile:
The curve forming the face and the flank is called profile

## Slide 32
Ease of manufacture | Easy to manufacture (because curve is single curve) | Difficult to manufacture (because curve is not single curve)
Centre distance | Do not require exact centre distance (for angular velocity) | Require exact centre distance (for angular velocity)
Interference | May occur | No Interference
Strength | Less (because radial flank) | More (because spreading flanks)

## Slide 33
Wear | More | Less
Running | Smooth | Less smooth
Basic form | Constant for all gears | Variable depending upon gear ratio
Path of contact | Straight line | Curve

## Slide 34
For constant angular velocity ratio of the two gears, the common normal at the point of contact of the two mating teeth must pass through the pitch point.
LAW OF GEARING
A point C on the tooth profile of gear 1 is in contact with a point D on the tooth profile of gear 2. The two curves in contact at point C or D must have a common normal at the point. Let it be n - n.

## Slide 35
Let
= instantaneous angular velocity of gear 1 (clockwise)
= instantaneous angular velocity of gear 2 (counter-clockwise)
= linear velocity of C
= linear velocity of D

## Slide 36
Then
= . A C in a direction perpendicular to A C or at an angle a to n - n
= . BD in a direction perpendicular to BD or at an angle p to n - n
Now, if the curved surfaces of the teeth of two gears are to remain in contact, one surface may slide relative to the other along the common tangent t - t. The relative motion between the surfaces along the common normal n-n must be zero to avoid the separation, or the penetration of the two teeth into each other.

## Slide 37
Component of Vc along n - n = Vc cos
Component of v d along n - n = vd cos
Relative motion along n - n = vc cos - vd cos
Draw perpendiculars AE and BF on n - n from points A and B respectively
Angle CAE =
Angle DBF =

## Slide 38
For proper contact,
Relative motion along n - n = vc cos - vd cos = 0

## Slide 39: VELOCITY OF SLIDING
if the curved surfaces of the two teeth of the gears 1 and 2 are to remain in contact, one can have a sliding motion relative to the other along the common gent t - t at C or D
Component of Vc along t-t = Vc sin
Component of v d along t-t = vd sin
Relative motion along t-t = vc sin - vd sin

## Slide 40
Velocity of sliding = vc sin - vd sin
= (Sum of the angular velocity)*(distance between the pitch point & the point of contact)
Since PC=PD

## Slide 41: Path of contact
It is the locus of point of contact of two mating teeth from the beginning of the engagement to the end of the engagement.
Path of approach:
It is the portion of path of contact from the beginning of the engagement to the pitch point.
Path of recess:
It is the portion of path of contact from pitch point to the end of engagement.
As shown in the fig. MN is the common tangent at to the base circle. It is equal to the common normal at the point of contact of two teeth. The addendum circle cuts the common tangent MN at point E & F. In other words contact of teeth begins at E & ends at F.

## Slide 45
Let,
O1P = Pitch circle radius of gear = R
O1E = Addendum circle radius of gear = RA
O1N = Base circle radius of gear = O1P cos = R cos
O2P = Pitch circle radius of pinion = r
O2E = Addendum circle radius of pinion = rA
O2N = Base circle radius of pinion = O2P cos = r cos
= Pressure angle
Length of path of contact = EF = EP + PF…(1)
Where,
EP = Path of approach
PF = Path of recess
Path of approach = EP = EN – PN ………(2)
From triangle O1PN,
PN = O1P sin = R sin
Join O1 to E and from triangle O1EN,
Substituting the values of PN & EN in equation (2)
Path of approach

## Slide 46
Path of recess = PF = MF – MP …………………(4)
From triangle O2MP,
PN = O2P sin = r sin
Join O1 to E and from triangle O2MF,
Substituting the values of MP & MF in equation (4)
Path of recess
Substituting the values of EP & PF in equation (1), we get
Path of contact
If the driver & driven have equal number of teeth, then the diameter of the driver & driven gears are same. Therefore for equal gears, the equation (6) becomes,

## Slide 47
Arc of contact
It is the locus of point on the pitch circle of two mating teeth from the beginning of the engagement to the end of the engagement. In Figure, the arc of contact is EPF or GPH.
Arc of approach:
It is the portion of arc of contact from the beginning of the engagement to the pitch point.
Arc of recess:
It is the portion of arc of contact from pitch point to the end of engagement.
Arc of contact = length of path of contact/ cos ……(8)

## Slide 48: Contact ratio
Ratio of angle of action to the pitch angle OR Average number of pairs of teeth which are in contact.
Contact ratio = CR =
length of path of contact
= ---------------------------------------
Base pitch
length of arc of contact
= ---------------------------------------
Circular pitch
length of path of contact
= ---------------------------------------
length of arc of contact
= ---------------------------------------
= Angle Of Action
= Angle Of Approach
= Angle Of Recess
= pitch Angle

## Slide 49: Interference in involutes gears
If the radius of the addendum circle of the pinion is increased to O1N, the point of contact L will move
When the axis is further increased, the point of contact L will be on the inside of the base circle of the wheel & not on the involute profile of the tooth on the wheel.
Similarly if the radius of the addendum circle of the wheel increases beyond the O2M, then the tip of the tooth on the wheel will cause interference with the pinion
Points M & N are called interference points
The phenomenon when the tip of tooth undercuts the root of its mating gear is known as interference OR contact of portion of the two tooth profiles which are not conjugate is called interference.

## Slide 50: Methods to avoid interference & its effects
Under cutting
Increasing the centre distance
By tooth correction
Height of the teeth may be reduced

## Slide 51: Minimum number of teeth required to avoid interference
Pinion turns counter-clockwise & drives the gear
CD = common tangent
C & D interference points
If the path of contact does not extend beyond either of these points, interference is avoided
O1D = limiting value of addendum circle radius of pinion
O2C = limiting value of addendum circle radius of gear
Each addendum circle radius is compared with its limiting value to determine whether there will be a interference
Interference likely to occur on pinion than on gear, and in this case, the critical radius is O2C, which limits the number of teeth on pinion

## Slide 52
O1P = pitch circle radius of pinion = r = mt/2
O2P = pitch circle radius of gear = R = mT/2
O2D = Base circle radius of gear = Rb
O2C = addendum circle radius gear = Ra
T = Number of teeth on gear
t = Number of teeth on pinion
aw = addendum constant of gear
ap = addendum constant of pinion
awm = addendum of gear
apm = addendum of pinion
G = gear ratio = T/t
From the right angle triangle O2CD,
O2C2 = O2D2 + CD2 = O2D2 + (CP+PD)2
= O2D2 + (O1P sin + 02P sin )2
R2a = R2b + (r sin + R sin )2
= (R cos )2 + (r + R)2 sin2
= R2 cos2 + r2 sin2 + R2 sin2 + 2 r R sin2
= R2 (cos2 + sin2 ) + r2 sin2 + 2 r R sin2
= R2 + r2 sin2 + 2 r R sin2

## Slide 53
Minimum number of teeth,
We know that,
GEAR RATIO ,G= N1/N2 = R/r = T/t
Number of teeth on gear to avoid interference is,
Addendum of Gear = awm = Ra -R

## Slide 54
Number of teeth on the pinion = t = T/G
If number of teeth on the pinion “t” is same as the number of teeth on gear “T”, then the gear ratio G is equal to one.
then equation (4) becomes,

## Slide 55: Involutometry
Study of the geometry of involute is called involutometry
Let B & C be two points on the involute
Normal from point B & C are tangent to the base circle
Let,
rA = base circle radius
rB= radius of point B on the involute
rC= radius of point C on the involute
= pressure angle for point B
= pressure angle for point C
tB= arc tooth thickness at B
tC= arc tooth thickness at C

## Slide 56
From triangle OBE,
From triangle OCF,
Equating (1) & (2)
From The Geometry (By the properties of the involute)
Arc AE = Length BE
Arc AF = Length CF
Now from fig.,
Angle AOE = Arc AE/OE = BE/OE = tan

## Slide 57
Now from fig.,
Angle AOF = Arc AF/OF = CF/OF = tan
From fig., for point B,
Similarly for point C,
Equating (6) & (7)
S=rθ
S is tB
r is rB

## Slide 58: Backlash
It is the difference between the thickness of the tooth & the width of the tooth space in which it meshes.
Backlash must be allowed to prevent jamming of the teeth
Back lash = space width – tooth thickness

## Slide 60
Let, P’ be the new pitch point
r = standard pitch circle radius of pinion
R= standard pitch circle radius of gear
c = standard centre distance = R + r
r’ = operating pitch circle radius of pinion
R’ = operating pitch circle radius of gear
c’ = operating centre distance = R’ + r’
= standard pressure angle
= operating pressure angle
h = tooth thickness of pinion on standard pitch circle =p/2
h’ = tooth thickness of pinion on operating pitch circle
H = tooth thickness of gear on standard pitch circle =p/2
H’ = tooth thickness of gear on operating pitch circle
p = standard circular pitch =
p’ = operating circular pitch =
= change in centre distance
B = backlash
T = number of teeth on gear
t = number of teeth on pinion
c

## Slide 61
We know,
On the operating pitch circle,
Operating pitch = sum of the tooth thickness + backlash
i.e. p’ = h’ + H’ + B ………………………….(1)
By involutometry,
Since H=h=P/2

## Slide 62
Substituting The Values of H’ & h’ inn equation (1),

## Slide 63: Problems
A spur gear of 200 pressure angle running at 200 rpm drives another gear at a speed of 100 rpm. The centre distance between the two gears is 300 mm & module is 10 mm. Standard addendum = 1m. Determine:
  Pitch circle radius of pinion
  Pitch circle radius of gear
  No. of teeth on gear
  No. of teeth on pinion
  Base circle radius of gear
  Base circle radius of pinion
  Circular pitch
  Tooth thickness on pitch circle for no backlash
  Pitch line velocity (rolling velocity)
  Length of path of contact
  Length of arc of contact
  Contact ratio (no. of pairs of teeth in contact)
  Velocity of sliding at the point of
    Engagement
    Pitch point
    Disengagement

## Slide 64
Angle of action (angle turned by the pinion & gears)
No. of teeth to avoid interference & max. velocity of sliding
Ratio of sliding velocity to rolling velocity at the instant of
  Engagement
  Pitch point
  Disengagement
Tooth thickness at the base circle radius
Tooth thickness at addendum circle radius
If the centre distance is increased by 0.6 m find,
  Operating pitch circle radii
  Operating pressure angle
  backlash