## Slide 1
The process in which the desired shape and size are obtained through plastic deformation of the material.
Very economical process as the desired shape, size and finish can be obtained without significant loss of material.
Also improves the strength of the product through strain hardening.
METAL FORMING

## Slide 2
Rubber pad forming
Rubber pad forming (RPF) is a metalworking process where sheet metal is pressed between a die and a rubber block, made of polyurethane.

## Slide 3
Under pressure, the rubber and sheet metal are driven into the die and conform to its shape, forming the part.
The rubber pads can have a general purpose shape, like a membrane. Alternatively, they can be machined in the shape of die or punch.
Due to the material properties of the rubber, the pad will regain its original shape when retracted from the tool.

## Slide 4
In general, an elastic upper die, usually made of rubber, is connected to a hydraulic press.
Rubber pad forming can be accomplished in many different ways.
A rigid lower die, often called a form block, provides the mold for the sheeted metal to be formed.
The rubber exerts nearly equal pressure on all work piece surfaces due to its incompressibility.
The multidirectional nature of the force from the rubber pad produces variable radius during forming and thus enhances uniform elongation of the work piece.

## Slide 5
Types of Rubber pad forming processes
Guerin process
Marform deep drawing process
Verson Hydroform process
Masleennikov’s process

## Slide 6
Guerin process
As the ram descends, the rubber presses the blank around the form block, thus forming the work piece.
The rubber-pad retainer fits closely around the platen, forming an enclosure that traps the rubber as pressure is applied.
Oldest and simplest rubber pad forming process.
Aluminum alloys, Austenitic Stainless Steels and titanium alloys can be shallow drawn using this process.
The pressure produced in the Guerin process is ordinarily between 6.9 and 48 MPa.

## Slide 7
This process is however limited to forming moderately shallow, recessed parts, having simple flanges and having simple configuration due to lower strength of rubber.
Guerin process

## Slide 8
Guerin Process
Advantages of Guerin Process
Low tooling cost
Form block can be made of wood, plastic, or other materials that are easy to shape
Rubber pad can be used with different form blocks
Process attractive in small quantity production

## Slide 9
In Marform process, deep-recessed parts with either vertical or sloped walls can be formed.
Compared with Guerin process, tooling includes a steel blank holder supported
by a hydraulic actuator equipped with a valve controlling pressure.
Marform process

## Slide 10
Verson Hydroform process is different than other processes in the sense that it contains the die cavity which is partially filled with hydraulic fluid.
The forming pressure is balanced by fluid pressure.
More severe draws can be made by this method than in conventional draw dies because the oil pressure against the diaphragm causes the metal to be held tightly against the sides as well as against the top of the punch.
Verson Hydro form process
In this process, hydraulic pressure under control would act on rubber membrane covering the blank.

## Slide 11
In 1957, Masennikov introduced a punch less drawing technique using annular technique.
It is a deep drawing technique that uses annular rubber pad to draw very deep cups.
The punch squeezes the rubber ring and makes it deform radially inward.
It develops a radial frictional force between the rubber ring and the blank and causes the blank to draw inside the die cavity.
Maslennikov’s process

## Slide 12
Due to low hardness of the rubber pad, the worked metal is not worn as quickly as in more conventional processes such as deep drawing.
The great advantage is that only one tool is needed, the rubber takes over the function of the counter die and the blank holder.
This results in low tooling costs, a short time to market and minimal damage of the material surface.
ADVANTAGES
Because the upper (male) die can be used with separate lower (female) dies, the process is relatively cheap and flexible.

## Slide 13
LIMITATIONS
Lower forming pressure and consequently large amount of wrinkles.
Low production rate
Since the amount of pressure exerted by rubber is limited by the strength of rubber itself, forming of sheet metal parts with small forming radius may not be possible.
The wear of the rubber is an issue in larger quantity manufacturing.

## Slide 14
Rubber pad forming has been used in production lines for many years.
Up to 60% of all sheet metal parts in the aerospace industry are fabricated using this process.
The most relevant applications are aerospace, automotive and defense fields.
It is frequently used in prototyping and production of small quantities of sheet metal parts.
APPLICATIONS