## Slide 1
        Introduction
        Photovoltaic effect
        Electron-hole formation
        A solar panel (or) solar array
        Types of Solar cell
        Principle, construction and working of Solar cell
        Advantage, disadvantage and application

## Slide 2
Recap (Lecture-1) : Photo means light in Greek and Volt is the name of a pioneer in the study of electricity Alessandro Volta
Solar cell: Solar cell is a photovoltaic device that converts the light energy into electrical energy based on the principles of photovoltaic effect
Albert Einstein was awarded the 1921 Nobel Prize in physics for his research on the photoelectric effect—a phenomenon central to the generation of electricity through solar cells.
In the early stages, the solar cell was developed only with 4 to 6 % efficiency( because of inadequate materials and problems in focusing the solar radiations). But, after 1989, the solar cells with more than 50% efficiency was developed.
1. Introduction

## Slide 3: Three generations of solar cells
First Generation
First generation cells consist of large-area, high quality and single junction devices.
First Generation technologies involve high energy and labour inputs which prevent any significant progress in reducing production costs.

## Slide 4: Second Generation Second generation materials have been developed to address energy requirements and production costs of solar cells. Alternative manufacturing techniques such as vapour deposition and electroplating are advantageous as they reduce high temperature processing significantly

## Slide 5
Materials for Solar cell
Solar cells are composed of various semiconducting materials
  Crystalline silicon
  Cadmium telluride
  Copper indium diselenide
  Gallium arsenide
  Indium phosphide
  Zinc sulphide
Note: Semiconductors are materials, which become electrically conductive when supplied with light or heat, but which operate as insulators at low temperatures

## Slide 6
Over 95% of all the solar cells produced worldwide are composed of the semiconductor material Silicon (Si). As the second most abundant element in earth`s crust, silicon has the advantage, of being available in sufficient quantities.
To produce a solar cell, the semiconductor is contaminated or "doped".
"Doping" is the intentional introduction of chemical elements into the semiconductor.
By doing this, depending upon the type of dopant, one can obtain a surplus of either positive charge carriers (called p-conducting semiconductor layer) or negative charge carriers (called n-conducting semiconductor layer).

## Slide 7
If two differently contaminated semiconductor layers are combined, then a so-called p-n-junction results on the boundary of the layers.
By doping trivalent element, we get p-type semiconductor. (with excess amount of hole)
By doping pentavalent element, we get n-type semiconductor ( with excess amount of electron)
n-type semiconductor
p- type semiconductor
p-n junction layer

## Slide 8
2. Photovoltaic effect
Definition:
The generation of voltage across the PN junction in a semiconductor due to the absorption of light radiation is called photovoltaic effect. The Devices based on this effect is called photovoltaic device.
Light energy
n-type semiconductor
p- type semiconductor
Electrical Power
p-n junction

## Slide 9
3. electron-hole formation
Photovoltaic energy conversion relies on the number of photons strikes on the earth. (photon is a flux of light particles)
On a clear day, about 4.4 x 1017 photons strike a square centimeter of the Earth's surface every second.
Only some of these photons - those with energy in excess of the band gap - can be converted into electricity by the solar cell.
When such photon enters the semiconductor, it may be absorbed and promote an electron from the valence band to the conduction band.

## Slide 10
Therefore, a vacant is created in the valence band and it is called hole.
Now, the electron in the conduction band and hole in valence band combine together and forms electron-hole pairs.
    hole
Valence band
Conduction band
electron
Photons

## Slide 11
4. A solar panel (or) Solar array
Single solar cell
The single solar cell constitute the n-typpe layer sandwiched with p-type layer.
The most commonly known solar cell is configured as a large-area p-n junction made from silicon wafer.
A single cell can produce only very tiny amounts of electricity
It can be used only to light up a small light bulb or power a calculator.
Single photovoltaic cells are used in many small electronic appliances such as watches and calculators

## Slide 12
N-type
P-type
Single Solar cell

## Slide 13
Solar panel (or) solar array (or) Solar module
The solar panel (or) solar array is the interconnection of number of solar module to get efficient power.
A solar module consists of number of interconnected solar cells.
These interconnected cells embedded between two glass plate to protect from the bad whether.
Since absorption area of module is high, more energy can be produced.

## Slide 15
Based on the types of crystal used, soar cells can be classified as,
      Monocrystalline silicon cells
      Polycrystalline silicon cells
      Amorphous silicon cells
The Monocrystalline silicon cell is produced from pure silicon (single crystal). Since the Monocrystalline silicon is pure and defect free, the efficiency of cell will be higher.
In polycrystalline solar cell, liquid silicon is used as raw material and polycrystalline silicon was obtained followed by solidification process. The materials contain various crystalline sizes. Hence, the efficiency of this type of cell is less than Monocrystalline cell.
5. Types of Solar cell

## Slide 16
Amorphous silicon was obtained by depositing silicon film on the substrate like glass plate.
The layer thickness amounts to less than 1µm – the thickness of a human hair for comparison is 50-100 µm.
The efficiency of amorphous cells is much lower than that of the other two cell types.
  As a result, they are used mainly in low power equipment, such as watches and pocket calculators, or as facade elements.

## Slide 17
Comparison of Types of solar cell
Material | Efficiency (%)
Monocrystalline silicon | 14-17
Polycrystalline silicon | 13-15
Amorphous silicon | 5-7

## Slide 18
6. Principle, construction and working of Solar cell
Principle: The solar cells are based on the principles of photovoltaic effect.The photovoltaic effect is the photogeneration of charge carriers in a light absorbing materials as a result of absorption of light radiation.
Construction
Solar cell (crystalline Silicon) consists of a n-type semiconductor (emitter) layer and p-type semiconductor layer (base). The two layers are sandwiched and hence there is formation of p-n junction.
The surface is coated with anti-refection coating to avoid the loss of incident light energy due to reflection.

## Slide 21
A proper metal contacts are made on the n-type and p- type side of the semiconductor for electrical connection
Working:
When a solar panel exposed to sunlight , the light energies are absorbed by a semiconduction materials.
Due to this absorded enrgy, the electrons are libereted and produce the external DC current.
The DC current is converted into 240-volt AC current using an inverter for different applications.

## Slide 22
Mechanism:
First, the sunlight is absorbed by a solar cell in a solar panel.
The absorbed light causes electrons in the material to increase in energy. At the same time making them free to move around in the material.
However, the electrons remain at this higher energy for only a short time before returning to their original lower energy position.
Therefore, to collect the carriers before they lose the energy gained from the light, a PN junction is typically used.

## Slide 23
A PN junction consists of two different regions of a semiconductor material (usually silicon), with one side called the p type region and the other the n-type region.
During the incident of light energy, in p-type material, electrons can gain energy and move into the n-type region.
Then they can no longer go back to their original low energy position and remain at a higher energy.
The process of moving a light- generated carrier from p-type region to n-type region is called collection.
These collections of carriers (electrons) can be either extracted from the device to give a current, or it can remain in the device and gives rise to a voltage.

## Slide 24
The electrons that leave the solar cell as current give up their energy to whatever is connected to the solar cell, and then re-enter the solar cell. Once back in the solar cell, the process begins again:

## Slide 25
The mechanism of electricity production- Different stages
Conduction band High density
Valence band Low density
E
The above diagram shows the formation of p-n junction in a solar cell. The valence band is a low-density band and conduction band is high-density band.

## Slide 26
Stage-1
Therefore, the hole (vacancy position left by the electron in the valence band) is generates. Hence, there is a formation of electron-hole pair on the sides of p-n junction.
When light falls on the semiconductor surface, the electron from valence band promoted to conduction band.
Conduction band High density
Valence band Low density
E

## Slide 27
Stage-2
In the stage 2, the electron and holes are diffuse across the p-n junction and there is a formation of electron-hole pair.
Conduction band High density
Valence band Low density
E
junction

## Slide 28
Stage-3
In the stage 3, As electron continuous to diffuse, the negative charge build on emitter side and positive charge build on the base side.
Conduction band High density
Valence band Low density
E
junction

## Slide 29
Stage-4
When the PN junction is connected with external circuit, the current flows.
Conduction band High density
Valence band Low density
E
junction
Power

## Slide 30
7. Advantage, disadvantage and application of Solar cell
Advantage
    It is clean and non-polluting
    It is a renewable energy
    Solar cells do not produce noise and they are totally silent.
    They require very little maintenance
    They are long lasting sources of energy which can be used almost anywhere
    They have long life time
    There are no fuel costs or fuel supply problems

## Slide 31
Disadvantage
    Solar power can not be obtained in night time
    Solar cells (or) solar panels are very expensive
    Energy to be stored in batteries
    Air pollution and weather can affect the production of electricity
    They need large area of land to produce more efficient power supply

## Slide 32
Applications
    Soar pumps are used for water supply.
    Domestic power supply for appliances include refrigeration, washing machine, television and lighting
    Ocean navigation aids: Number of lighthouses and most buoys are powered by solar cells
    Telecommunication systems: radio transceivers on mountain tops, or telephone boxes in the country can often be solar powered
    Electric power generation in space: To providing electrical power to satellites in an orbit around the Earth