## Slide 1: UNIT-5
OCEAN THERMAL ENERGY CONVERSION

## Slide 2
THE surface of water acts as collector for solar heat while the upper layer of the sea is infinite heat storage reservoir.
Due to the temperature difference between warm surface and colder depth of ocean water 20-25K.
Warm surface water could be used to heat low boiling point organic fluid which can run the heat engine.
The exit vapour would condense by pumping cold water from deeper regions.

## Slide 3: Methods of harnessing OTEC:
1.OPEN CYCLE(claude cycle)
2.CLOSED CYCLE(Anderson cycle)
1.Open cycle
In open cycle water is the working fluid.The warm surface water is caused to boil by lowering the pressure without supplying any additional heat.The steam drives the turbine and exhaust steam is condensed by deep colder water.